## Slide 1: BJT (Bipolar Junction Transistor)

## Slide 2
Point-Contact Transistor –
first transistor ever made

## Slide 3
The transistor was probably the most important invention of the 20th Century.
The story behind the invention is one of clashing egos and top secret research.
First - BJTs
Reference:
Bell Labs Museum
B. G. Streetman & S. Banerjee ‘Solid State Electronic Devices’, Prentice Hall 1999.

## Slide 4
Picture shows the workbench of John Bardeen (Stocker Professor at OU) and Walter Brattain at Bell Laboratories.
The experimental results hadn't been very good. Their boss, William Shockley, came near to canceling the project. But in 1947, they built the circuit in the picture.
It was a working amplifier! John and Walter submitted a patent for the first working point contact transistor.
Interesting story…

## Slide 5
Shockley was furious and took their work and invented the junction transistor and submitted a patent for it 9 days later.
The three shared a Nobel Prize in 1955. Bardeen and Brattain continued in research (and Bardeen later won another Nobel).
Shockley quit to start a semiconductor company in Palo Alto. It folded, but its staff went on to invent the integrated circuit (the "chip") and to found Intel Corporation.
By 1960, all important computers used transistors for logic, and ferrite cores for memory.
Interesting story…

## Slide 6: Recall p-n junction
P
N
W
Vappl > 0
-
+
N
P
W
Vappl < 0
-
+
Forward bias, + on P, - on N
(Depletion region shrinks and then disapper.
Allow holes to jump over barrier
into N region.
Reverse bias, + on N, - on P
(Depletion region expandsi)
Remove holes and electrons away
from depletion region
I
V
I
V

## Slide 7: So if we combine these by fusing their terminals…
P
N
W
Vappl > 0
-
+
N
P
W
Vappl < 0
-
+
Holes from P region of 1st PN junction are
driven by Forward Bias of 1st PN junction into central N region
Holes in the central N region are attracted by the negative terminal of the Reverse Bias of the 2nd junction.
Forward Bias
Reverse Bias

## Slide 8
Basic models of BJT
Diode
Diode
Diode
Diode
npn transistor
pnp transistor

## Slide 9: npn BJTs
It contains three semiconductor layers: one p-layer and two n-layers.
The area of collector layer is largest. So it can dissipate heat quickly.
Area of base layer is smallest and it is very thin.
Area of emitter layer is medium.
Collector layer is moderately doped. So it has medium number of charges (electrons).
Base layer is lightly doped. So it has a very few number of charges (holes).
Emitter layer is heavily doped. So it has largest number of charges (electrons).
THE P-LAYER IS SANDWICHED BETWEEN TWO N-LAYERS.
The junction between collector layer and base layer is called as collector-base junction or c-b junction.
The junction between base layer and emitter layer is called as base-emitter junction or b-e junction.
The two junctions have almost same potential barrier voltage of 0.6V to 0.7V, just like in a general purpose diode.
collector layer
emitter layer
base layer

## Slide 10: npn BJTs
The collector is connected to high positive voltage with respect to base i.e. Vcb is very high. So c-b junction is reverse biased.
When we increase Vbe ≥ 0.7V (the value 0.7V is a typical value of potential barrier voltage) the transistor (b-e junction) is forward biased.
Now large number of electrons in emitter layer is repelled by negative terminal of Vbe and they flow towards b-e junction.
They cross the junction and enter into small base layer. Here some electrons combine with holes. Also some of them are attracted by positive terminal of Vbe and remaining maximum number of electrons flow into collector layer, crossing the second junction i.e. c-b junction.
The resident electrons of collector are repelled by these (guest) electrons and thus, then all the electrons are present in collector layer are attracted by positive terminal of Vcb. Thus, all these electrons complete their journey back into emitter layer and produce conventional currents in the transistor as shown in the above circuit.

## Slide 11: npn BJTs
Now when Vbe is still increased, more electrons are repelled by negative terminal of Vbe. So base-emitter junction is more and more forward biased. Thus, base (Ib) and collector currents (Ic) increase.
Collector current (Ic) is the function of base current (Ib).
In all this process, maximum number of electrons from emitter layer flow into collector layer. So collector current is ALMOST EQUAL to emitter current. Hence we say that, collector current is proportional to emitter current.

## Slide 12: BJT Currents

## Slide 13: Bipolar Junction Transistors: Operation Modes
Bias Mode | E-B Junction | C-B Junction
Saturation | Forward | Forward
Active | Forward | Reverse
Cutoff | Reverse | Reverse
Saturation : In this method both the junctions are forward biased. This method is not useful as the transistor is in “saturation” and the current cannot be controlled easily.
Cutoff: In this method both the junctions are reverse biased. This method is also not useful as the transistor is in “cut-off” state since current is zero.
Active: This is the most common and popular method used in transistor biasing. In this method, the base-emitter junction is forward biased and collector-base junction is reverse biased. So by adjusting base voltage we can control total current in the transistor easily.
Operational modes are defined based on VBE and VBC

## Slide 14
BJT Operating Regions and I V Curves
Input characteristics
  the input takes the form of a forward-biased pn junction
  the input characteristics are similar to a semiconductor diode
Output characteristics
  region near to the origin is the saturation region
  this is normally avoided in linear circuits

## Slide 15
Operation mode: vBE is forward & vBC is reverse (Active mode)
The Shockley equation
IES=saturation current (10-12-10-16A); VT=kT/q -thermal V (26mV)
The Kirchhoff’s laws
It is true regardless of the bias
conditions of the junction
Useful
parameter
BJTs – Current & Voltage Relationships

## Slide 16
Relationship between the collector current and the base current
  characteristic is approximately linear
  magnitude of collector current is generally many times that of the base current
  the device provides current gain
It is true regardless of the bias
conditions of the junction
Useful
parameter

## Slide 17
Please calculate the current gain () of this transistor
Example:

## Slide 18
Voltage polarities and current flow
if transistors are biased in the active mode.
Notes: sedr42021_0514a.jpg

## Slide 19
BJTs – Characteristics
npn transistor
Input
Output
if VC<VB and VE<VB, BC and BE junctions are forward biased, respectively (saturation region)
Remember VBE has to be greater than 0.6-0.7 V
VCE>VBE , B-C junction is reverse biased. VE<VB ,BE junction is forward biased (active region)

## Slide 20
BJTs – Load line analysis
Input loop
if iB=0
if vBE=0
vBB
VBB/RB

## Slide 21
BJTs – Load line analysis
Output loop

## Slide 22
or
Assumption:
It is assumed that |VBE| = 0.7V in the active and saturation regions.
Load Line Analysis:
Can be performed in order to determine |VBE| value of transistor in the active and saturation regions.

## Slide 23
Problem : Analyze the circuit shown in figure to determine current (I) and voltage (V) values. For the transistor, assume that β = 100 and
|VBE| = 0.7V in the active region. (RC=5kΩ, RE=7.07kΩ)
Notes: sedr42021_0515a.jpg

## Slide 24
Problem : Analyze the circuit shown in Figure to determine I and V values. For the transistor, assume that β = 100 and |VBE| = 0.7V in the active region.
Notes: sedr42021_0515a.jpg

## Slide 25
Early Effect
Ideal: Slope is zero
Reallity: Slope is not zero. This nonlinear behaviour is modeled by ‘Early Voltage’ (VA).
Early Effect

## Slide 26: DC Biasing Circuits of BJTs

## Slide 27: Objectives
State the purpose of DC biasing circuits.
Plot the DC load line for the given the value of VCC .
Describe the Q-point of an amplifier.
Describe and analyze the operations of various bias circuits:
  base-bias circuits
  voltage-divider bias circuits
  emitter-bias circuits
  collector-feedback bias circuits
  emitter-feedback bias circuits

## Slide 28: A generic DC load line.

## Slide 29: Example
Plot the DC load line for the circuit shown in Figure.

## Slide 30: Example
Plot the DC load line for the circuit shown in Fig. Then, find the values of VCE for IC = 1, 2, 5 mA respectively.
IC (mA) | VCE (V)
1 | 9
2 | 8
5 | 5
Different operating points

## Slide 31: Optimum Q-point with amplifier operation.

## Slide 32: Q-point is not at optimum location
Clipping
Clipping
Amplitude of input signal can not be too great
Min Vce voltage
Max Ic current

## Slide 33: BIAS CIRCUITS
b = DC current gain = hFE
1. Base bias (fixed bias).
Assumption:
|VBE| = 0.7V

## Slide 34: Example
Construct the DC load line for the circuit and plot the Q-point. Determine whether the circuit is midpoint biased.

## Slide 35: Example Construct the DC load line for the circuit
The circuit is midpoint biased.

## Slide 36: (Q-point shift)
The transistor has values of hFE = 100 when T = 25 °C and hFE = 150 when T = 100 °C. Determine the Q-point values of IC and VCE at both of these temperatures. VBE=0.7V
Temp(°C) | IB (mA) | IC (mA) | VCE (V)
25 | 20.28 | 2.028 | 3.94
100 | 20.28 | 3.04 | 1.92
(250C)
Q(1000C)

## Slide 37: Base bias characteristics.
Advantage: Circuit simplicity.
Disadvantage: Q-point shift with temp.
Applications: Switching circuits only.
Circuit recognition: A single resistor (RB) between the base terminal and VCC. No emitter resistor.

## Slide 38: 2. Voltage divider bias.
Assume that I2 > 10IB. Therefore, we can neglect IB
Assume that ICQ  IE (hFE >> 1). Then
Operating point
Assumption:
|VBE| = 0.7V

## Slide 39: Example
Determine the values of ICQ and VCEQ for the circuit shown in Fig.
Because ICQ @ IE (or hFE >> 1),
Assumption:
|VBE| = 0.7V

## Slide 40: Example
Verify that I2 > 10 IB

## Slide 41: Which value of hFE do I use?
Transistor datasheet may list any combination of the following hFE max, hFE min or hFE typ. Use typical value if there is one. Otherwise, use

## Slide 42: Example
A voltage-divider bias circuit has the following values:
R1 = 1.5 kΩ, R2 = 680 Ω, RC = 260 Ω, RE = 240 Ω and VCC = 10 V. Assuming the transistor is a 2N3904, determine the value of IB for the circuit.

## Slide 43: Stability of Voltage Divider Bias Circuit
The Q-point of voltage divider bias circuit is less dependent on hFE than that of the base bias (fixed bias).
For example, if IE is exactly 10 mA and the range of hFE is from 100 to 300. Then,
ICQ hardly changes over the entire range of hFE.
IE is determined by VCC, R1, R2 and VBE voltage of transistor. Their values hardly change with the change of temperature.

## Slide 44: Load line for voltage divider bias circuit.
Circuit values are from previous example.

## Slide 45: Voltage-divider bias characteristics.
Circuit recognition: The voltage divider in the base circuit.
Advantages: The circuit Q-point values are stable against changes in hFE.
Disadvantages: Requires more components than most other biasing circuits.
Applications: Used primarily to bias linear amplifier.

## Slide 46: 3. Emitter bias.
Assume that the transistor operation is in active region.
Assume that hFE >> 1.

## Slide 47: Example
Determine the values of ICQ and VCEQ for the amplifier shown in Fig.

## Slide 48: Load Line for Emitter-Bias Circuit
Assume that hFE >> 1.

## Slide 49: Circuit Stability of Emitter-Bias Circuit
hFE increases
IC and IE increase (if IB is the same)
VE and then VB increase
IB decreases
IC does not increase that much.
Good Stability. Less dependent on hFE and temperature.

## Slide 50: Emitter-bias characteristics.
Circuit recognition: A split (dual-polairty) power supply and the base resistor is connected to ground.
Advantage: The circuit Q-point values are stable against changes in hFE.
Disadvantage: Requires the use of dual-polarity power supply.
Applications: Used primarily to bias linear amplifiers.

## Slide 51: 4. Collector-feedback bias.

## Slide 52: Example
Determine the values of ICQ and VCEQ for the amplifier shown in Fig.

## Slide 53: Circuit Stability of Collector-Feedback Bias
hFE increases
IC increases (if IB is the same)
VCE decreases
IB decreases
IC does not increase that much.
Good Stability. Less dependent on hFE and temperature.

## Slide 54: Collector-Feedback Characteristics
Circuit recognition: The base resistor is connected between the base and the collector terminals of the transistor.
Advantage: A simple circuit with relatively stable Q-point.
Disadvantage: Relatively poor AC characteristics.
Applications: Used primarily to bias linear amplifiers.

## Slide 55: 5. Emitter-feedback bias.

## Slide 56: Example

## Slide 57: Circuit Stability of Emitter-Feedback Bias
hFE increases
IC , IE increases (if IB is the same)
VE increases
IB decreases
IC does not increase that much.
IC is less dependent on hFE and temperature.

## Slide 58: Emitter-Feedback Characteristics
Circuit recognition: Similar to voltage divider bias with R2 missing (or base bias with RE added).
Advantage: A simple circuit with relatively stable Q-point.
Disadvantage: Requires more components than collector-feedback bias.
Applications: Used primarily to bias linear amplifiers.

## Slide 59
BJTs – Testing

## Slide 60
npn
BJTs – Practical Aspects

## Slide 62
npn
y
y

## Slide 63
npn

## Slide 64: Problem : Analyze the circuits shown in Figure to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in the active region.

## Slide 65
Consider the amplifier circuit shown below. Use the following parameters for your calculations. Transistor parameters : β=150, |VBE|=0.6V
a. Perform DC analysis and calculate DC operating values of the transistor.

## Slide 66: Problem: Consider the emitter-follower amplifier of figure. Draw the DC circuit and find ICQ (β = 100, VBE=0.7V).
I1

## Slide 67
Problem : Analyze the circuits shown in figure to determine I and V. For all transistors, assume that β = 100 and |VBE| = 0.7V in the active region.

## Slide 68: Problem: Suppose that npn transistor has VBE = 0.7V. Determine IC and VCE and output voltage.
Assume that Base current is small, so
Emitter voltage
VE = VB – VBE = 2.7 – 0.7 = 2.0 V
Emitter current
Since IB is small, collector current IC  IE = 2 mA
Output voltage = VCC – ICRC = 10 - 2 mA 2.2 k = 5.6 V

## Slide 69: Problem: The transistors shown in figure operate in active region and have β = 100, VBE=0.7V. Determine IC and VCE for each transistor.
I1
IE2
VBE
15V- IB1 1.43MΩ-VBE1 =0 => IB1 SOLVED
15V-(IC1+IB2)10kΩ-VBE2 – (β+1) IB2 1kΩ =0 => IB2 SOLVED
15V- IC2 1kΩ-VCE2 – (β+1) IB2 1kΩ =0 => VCE2 SOLVED

## Slide 70: Problem: Analyze the circuit of figure and determine IC and VCE. (β = 100, VBE=0.7V)
VB = 0.7V
15V- (IB + β IB + I1) 4.7kΩ- (IB + I1) 47kΩ = VB
=> IB SOLVED
VB - I1 150KΩ = -15V => I1 SOLVED
15V- (IB + β IB + I1) 4.7kΩ- VCE = 0
=> VCE SOLVED

## Slide 71
Current Mirror
The following circuits show how matched transistors, when combined with a few resistors, can act as current sources.
A current mirror is a circuit designed to copy a current through one active device by controlling the current in another active device of a circuit, keeping the output current constant regardless of loading.

## Slide 72
Current Mirror

## Slide 73
Current Mirror Equations considering Early Effect
(VCE2)
(IC2)
VCE1 =VBE1

## Slide 74
Finite output resistance

## Slide 75
Current Mirror

## Slide 76: Noise in Audio Amplifier
Consider the amplifier below which amplifies an audio signal from a microphone.
If the power supply (VCC) is time-varying, it will result in an additional (undesirable) voltage signal at the output, perceived as a “humming” noise by the user.

## Slide 77: Supply Ripple Rejection
Since node X and Y each see the voltage ripple, their voltage difference (Vout) will be free of ripple. Transistors are exactly same.

## Slide 78: BJT Differential Pair
With the addition of a “tail current,” an elegant and robust differential pair is achieved. Transistors are exactly the same.

## Slide 79: Differential Amplifiers

## Slide 80: Differential Amplifiers

## Slide 81
Graphical construction for the determination of the collector current (output)
Graphical construction for the determination of the base current (input)
Small-Signal Analysis
What happens is a small signal vi is superimposed on the DC voltage
Notes: sedr42021_0527.jpg

## Slide 82
Graphical determination of the signal components vbe, ib, ic, and vce when a signal component vi is superimposed on the dc voltage VBB
Small-Signal Analysis
Superimposed vi
Load line for min. vi value
Notes: sedr42021_0530a.jpg

## Slide 83
Small-Signal Equivalent Circuit (hybrid-π small-signal model)
Small signal equivalent circuit for npn BJT:
and
Transistor is modeled by using input resistance and output current
Assumption: Early Voltage (VA) is infinite.
/(β+1)
Slope=

## Slide 84
Early Effect
βib
Small signal equivalent circuit
This nonlinear behaviour is modeled by a resistor.
ICQ,VCEQ

## Slide 85: Two versions of the hybrid-π small-signal model

## Slide 86
DC ANALYSIS
Replace all capacitors with OPEN circuits.
Set all AC sources to zero, because they have zero signal component!!!
RS
R1
RC
R2
Cin
Cout
+
vs
-
+
RL vo
-
Q1
vin
+
-
CE
VCC
RE

## Slide 87
Constructing the Small-Signal Equivalent Circuit
To construct small-signal equivalent circuit for entire amplifier, we:
Replace the BJT by its small-signal model.
Replace all capacitors with short circuits.
Set all DC sources to zero, because they have zero signal component!!!
The result is the small-signal equivalent circuit of the amplifier:
RS
R1
RC
R2
Cin
Cout
+
vs
-
+
RL vo
-
Q1
vin
+
-
CE
VCC
RE

## Slide 88
First perform DC analysis to find small-signal equivalent parameters at the operating point.
Then:
To construct small-signal equivalent circuit for entire amplifier, we:
Replace the BJT by its small-signal model.
Replace all capacitors with short circuits.
Set all DC sources to zero, because they have zero signal component!!!
Small-Signal Analysis
The result is the small-signal equivalent circuit of the amplifier.

## Slide 89
Small-Signal Analysis
Avoc: Open circut gain. Gain without ‘Load’
Find voltage gain:

## Slide 90
Small-Signal Analysis
Find output impedance:
Z0 = vo / io=Rc
Find input impedance:

## Slide 91: Input/Output Impedances
The figure above shows the techniques of measuring input and output impedances.
When measuring output impedance, the input port has to be grounded.

## Slide 92: Input Impedance Example I
When calculating input/output impedance, small-signal analysis is assumed.

## Slide 93: Output Impedance Example I

## Slide 94: Impedance at Emitter
The impedance seen at the emitter of a transistor is approximately equal to one over its transconductance (if the base is grounded).

## Slide 95: Amplifier Circuits

## Slide 96
Common-Emitter (CE) Amplifier

## Slide 97: I/O Impedances of CE Amplifier
When measuring output impedance, the input port has to be grounded so that Vin = 0.

## Slide 98: Inclusion of Early Effect
Early effect will lower the gain of the CE amplifier, as it appears in parallel with RC.

## Slide 100
Consider an amplifier shown below. Suppose that the value of the coupling capacitors Cc1 and Cc2 are high enough, so they can be considered shorted in small signal analysis. Find the small signal values of Zin, Zout, and vout/vin.
NPN Transistor Parameters: VBE = 0.7, β = 40, VA = ∞, VT = 25 mV.
=
π
R1//R2
=>
rπ
R3
b
e
c
vin
βib
ib
ic
vout
ic
iin
vin
i0

## Slide 101
The parameters of the transistor are β = 100, VBE=0.7V and VA =∞.
(a) Find the DC voltages at the base and emitter terminals.
(b) Find RC such that VCEQ = 3.5 V.
(c) Assuming CC and CE act as short circuits, determine the small-signal voltage gain Av = vo /vs.

## Slide 102
Continue: The parameters of the transistor are β = 100, VBE=0.7V and VA =∞.
=
=>
RB
Rs
rπ
Rc
b
e
c
vs
βib
ib
ic
v0
ic

## Slide 103
RB
Rs
rπ
Rc
b
e
c
vi
βib
ib
ic
v0
iin
i0
Consider the amplifier shown above. Use the following parameters for your calculations. Transistor parameters : β=200, VBE=0.7V, VT=25mV, VA=∞
a. Find VB and V0 of the transistor by performing DC analysis.
b. Find the small signal values of Zin, Zout, and vo/vin.
5V- IB 400kΩ-VBE =0 => IB SOLVED
VBE =VB =0.7V
5V- β IB 1.2kΩ =V0 => V0 SOLVED
=
π

## Slide 104
By inserting a resistor in series with the emitter, this topology will decrease the gain of the amplifier but improve other aspects, such as linearity, and input impedance.
Emitter Degeneration

## Slide 105: Small-Signal Model
Base current is neglected
)

## Slide 106: Input Impedance of Degenerated CE Stage
With emitter degeneration, the input impedance is increased from r to r + (+1)RE; a desirable effect.

## Slide 107: Output Impedance of Degenerated CE Stage
Emitter degeneration does not alter the output impedance in this case.

## Slide 108: Emitter Degeneration Example I
The input impedance of Q2 can be combined in parallel with RE to yield an equivalent impedance that degenerates Q1.

## Slide 109: Emitter Degeneration Example II
In this example, the input impedance of Q2 can be combined in parallel with RC to yield an equivalent collector impedance to ground.

## Slide 110: Degenerated CE with Base Resistance

## Slide 111: Input/Output Impedances
Rin1 is more important in practice as RB is often the output impedance of the previous stage.

## Slide 112: Common Base (CB) Amplifier
In common base topology, where the base terminal is biased with a fixed voltage, emitter is fed with a signal, and collector is the output.

## Slide 113
The voltage gain of CB stage is gmRC, which is identical to that of CE stage in magnitude and opposite in phase.
Common Base (CB) Amplifier

## Slide 114: Input Impedance of CB Amplifier
The input impedance of CB stage is much smaller than that of the CE stage.
is neglected

## Slide 115: Output Impedance of CB Stage

## Slide 116: CB with Source Resistance
With an inclusion of a source resistor, the input signal is attenuated before it reaches the emitter of the amplifier; therefore, we see a lower voltage gain.
))

## Slide 117: Practical Example of CB Stage
An antenna usually has low output impedance; therefore, a correspondingly low input impedance is required for the following stage.

## Slide 118: Emitter Follower (Common Collector Amplifier)

## Slide 119: Small-Signal Model of Emitter Follower (Common Collector)
As shown above, the voltage gain is less than unity and positive.

## Slide 120: Input Impedance of Emitter Follower
The input impedance of emitter follower is exactly the same as that of CE stage with emitter degeneration. This is not surprising because the input impedance of CE with emitter degeneration does not depend on the collector resistance.

## Slide 121: Output Impedance of Emitter Follower
=

## Slide 122: Summary of Amplifier Topologies
The three amplifier topologies studied so far have different properties and are used on different occasions.
CE and CB have voltage gain with magnitude greater than one, while follower’s voltage gain is at most one.

## Slide 123: Amplifiers – Basic Amplifier Concepts

## Slide 124: Amplifiers – Basic Amplifier Concepts
Ideally, an amplifier produces an output signal with identical wave-shape as the input signal but with a larger amplitude.

## Slide 125: Amplifiers – Amplifier Model
Amplification can be modeled by a controlled source.
(gain without load)

## Slide 126: Amplifiers – Current and Voltage Gains
ii is the current delivered in to the terminals of the amplifier
i0 is the current flowing through the load

## Slide 127: Example

## Slide 128: Amplifiers – Cascade Amplifiers

## Slide 129: Example

## Slide 130: Example

## Slide 131: Amplifiers – Ideal Amplifiers

## Slide 132
Example

## Slide 133
Cascade Connection (cont.)
small signal gain is:
by determine the voltage gain at stages 1 & stage 2
therefore
input resistance
Output resistance

## Slide 134
Exercise
Draw the ac equivalent circuit and calculate the voltage gain, input resistance and output resistance for the cascade BJT amplifier in above Figure. Let the parameters are:

## Slide 135
Ac equivalent circuit for cascade amplifier
Solution:

## Slide 136
Solution:
DC analysis:
At Q1:
At Q2:
AC analysis:
At Q1:
At Q2:

## Slide 137
From the ac equivalent circuit:
At Q1, the voltage gain is:
Where is the voltage looking to the Q1 transistor
and is the resistance looking into Q2 transistor
Therefore
The voltage gain at Q1 is:
Solution:

## Slide 138
From the ac equivalent circuit:
At Q2, the voltage gain is:
Where is the voltage looking into the Q2 transistor
Therefore, the voltage gain at Q2 is:
The overall gain is then,
** The large overall gain can be produced by multistage amplifiers!!
So, the main function of cascade stage is to provided the larger overall gain
Solution:

## Slide 139
From the ac equivalent circuit:
The input resistance is:
The output resistance is:
Solution: