## Slide 1: Introduction to Electronics EHB222E

## Slide 2
Grading
Grading: Midterm Exams 2x 20%, Quizzes 2x 10%, Final Exam 40%
Midterm Exams: 30 October (could be after 5 pm, time to be arranged) and 10 December 2019
Pop Quizzes: 8 October and 26 November 2019 during regular class hours
Before the final exam the sum of your midterm exam grades should be larger than 50.

## Slide 3
Introduction
Semiconductors & Doping, Basics of pn junction
Diodes
BJT Transistors
MOSFET Transistors
Operational Amplifiers
Introduction to Electronics

## Slide 4: What is Electricity?
Electricity is generated from the motion of tiny charged atomic particles called electrons and protons!
Atoms contain
Protons (+)
Neutrons (0)
Electrons (-)

## Slide 5: What is Electricity?
Atoms contain
Protons (+)
Neutrons (0)
Electrons (-)
Protons are positively charged and electrons are negatively charged.
The unit of charge is Coulomb (C)

## Slide 6: Law of Electric Charges
The law of electric charges states that like charges repel, and opposite charges attract.
Protons are positively charged and electrons are negatively charged, so they are attracted to each other.
A negative charge has an inward electric field because it attracts positive charges.
The positive charge has an outward electric field, pushing away like charges.

## Slide 7: Electric Field
An electric field is the region around a charged object.
The force between the charged objects
is an electric force.
The size of the electric force depends on 2 things:
The amount of charge (the greater the charge, the greater the force)
The distance between charges (the further the distance, the less the force)

## Slide 8: Charged Objects
Atoms do not have a charge because the number of electrons and protons cancel each other out.
Example:
3 protons (+) & 3 electrons (-) = 0

## Slide 9: Charged Objects
How do objects get charged?
They either gain or lose electrons.
Why not protons?
Example:
3 protons (+) & 5 electrons (-) =
7 protons (+) & 2 electrons (-) =

## Slide 10
What is Current?
When electrons flows through a conductor,
Only some materials have free electrons inside and allow current flow.
Conductors:
YES!
Insulators:
NO!
No free electrons = No current
we call this flow as “current.”
silver
copper
gold
aluminium
iron
steel
brass
bronze
mercury
graphite
salty water
glass
rubber
oil
asphalt
fiberglass
porcelain
ceramic
quartz
(dry) cotton
(dry) paper
(dry) wood
plastic
air
diamond
pure water

## Slide 11: How Does Current Flow?
Current can only flow through conductors. Good conductors have low resistance so electrons flow through them with ease.
+++
Metal wires (conductors)
Current flow

## Slide 12: When Does Current NOT Flow?
+++
Plastic material (insulators)
Current cannot flow through insulators.
No current flow

## Slide 13: Note that Air is an Insulator
+++
Air
Current cannot flow through insulators
No current flow
That’s why a battery doesn’t discharge if left on its own.

## Slide 14: What is Voltage?
- measured in volts.
Voltage is the difference in energy level from one end of the battery (or any other energy source) to the other.
The energy difference causes the negative charges to move from a lover voltage level to higher voltage in a closed circuit

## Slide 15: A battery in an electrical circuit plays the same role as a pump in a water system.
A battery establishes a difference of potential that can pump electrons.
A battery pushes the electrons through the conductor.

## Slide 16: Current
Current is the amount of electric charge (coulombs) flowing through a cross section of a conductor in one second.
1 Ampere = 1 Coulomb/second
Electron flow is from a lower potential (voltage) to a higher potential (voltage).
Current flow is from a higher potential (voltage) to a lower potential (voltage).
higher potential
lower potential
Direction of current flow

## Slide 17
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
electron motion
Current direction
Sign Convention for Current Flow
Electrons carry negative charge
Current flow is in opposite direction

## Slide 18: Current Flow
The direction of current flow is indicated by an arrow.
Note: The voltage sources in the circuit flow current through nodes and wires.
+
_
DC Voltage Source
Current flow is from a higher potential (voltage) to a lower potential (voltage).
higher potential

## Slide 19
Conducting wires
Electronic elements
If two or more nodes are connected just by wires, intersection point can be considered as one single node.
Electric Circuit
Group of nodes connected only by wires
One big node
One big node
A single node
Nodes are Connected
by Wires Only
Intersection point of wires is call as a node
+
_

## Slide 20
I1 = I2 + I3
Diagram b shows a mechanical analogy
From Conservation of Charge
The sum of charges flowing into a node must be equal to the sum of the charges flowing out of the node.
Current is the amount of electric charge (coulombs) flowing through a cross section of a conductor in one second

## Slide 21: Kirchhoff’s Current Law
The sum of currents flowing into a node must be balanced by the sum of currents flowing out of the node.
i1
i2
i3
node
i1 flows into the node
i2 flows out of the node
i3 flows out of the node
i1 = i2 + i3
Gustav Kirchoff was an 18th century German mathematician
+
_

## Slide 22
i1 = i2 + i3 can also be written in the following form:
i1
i2
i3
node
Kirchhoff’s Current Law:
i1 – i2 – i3 = 0
(i2 and i3 leave the node, hence currents –i2 and –i3 enter the node.)
The sum of all the currents entering a node is zero.
+
_
DC Voltage Source

## Slide 23
2.5 mA
4 mA
i4
i2
i3
Example 1: Kirchhoff’s Current Law:
io
Q: How much is the current Io ?
A: io = 2.5 mA + 4 mA = 6.5 mA
The dotted circle is a node with 2.5 mA entering
Hence i2 = 2.5 mA exits the “node”.
Similarly, i3 = 4 mA.
From KCL, i4 = i2 + i3 = 6.5 mA, and Io = i4
DC Current Source

## Slide 24
Example 2: Kirchhoff’s Current Law:
Q: How much are the currents i1 and i2 ?
A: i2 = 10 mA – 3 mA = 7 mA
i1 = 10 mA + 4 mA = 14 mA
+
_
i1
4 mA
i2
10 mA
3 mA
node

## Slide 25
Sometimes Kirchhoff’s Current Law is abbreviated just by
KCL
The net current entering a node must be zero.
The sum of all currents entering a node must be zero.
Whatever flows into a node must come out.
Review: Different ways to state KCL:
more to follow…

## Slide 26
Voltage (Difference in energy level )
Voltages are measured across the nodes of a circuit.
The direction of a voltage is indicated by + and – signs.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
higher potential
lower potential

## Slide 27: Kirchhoff’s Voltage Law
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
The voltage measured between any two nodes does not depend of the path taken.
voltage
Example of KVL:
v1= v2 + v3
Similarly:
v1= v2 + v4
voltage
and:
v3= v4
voltage

## Slide 28
This equation can also be written in the following form:
Kirchhoff’s Voltage Law: v1 = v2 + v3
–v1 + v2 + v3 = 0
A formal statement of Kirchhoff’s Voltage Law:
The sum of voltages around a closed loop is zero.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–

## Slide 29: Using the Formal Definition of KVL
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
Sum the voltages that are encountered around the loop.
Define an arrow direction around a closed loop.
If the arrow first encounters a plus sign, enter that voltage with a (+) into the KVL equation.
If the arrow first encounters a minus sign, enter that voltage with a (–) into the KVL equation.
For the inner loop :
–v1 + v2 + v3 = 0
“The sum of voltages around a closed loop is zero.”
–v4 – v2 + v1 = 0
For the outer loop:

## Slide 30
Q: How much is the voltage Vo ?
A: Vo = 3.1 V + 6.8 V
Vo
_
+
+ 3.1V –
+
6.8V
–
Example 1: Kirchhoff’s Voltage Law:
A: v4 = 6.8 V
Q: How much is the voltage v4 ?
+
v4
_

## Slide 31
Example 2: Kirchhoff’s Voltage Law:
Q: If v1 = 10 V and v5 = 2 V, what are v2, v3, and v4?
-v1 + v2 = 0  v2 = 10 V
-v2 + v3 + v5 = 0  v3 = 10 V – 2 V = 8 V
-v4 + v5 = 0  v4 = 2 V
+
_
+
v1 = 10 V
–
+
v2
–
+
v4
–
+
v5= 2 V
–
+ v3 –

## Slide 32
Electronic Circuits
Circuits are obtained by connecting electronic elements
Typical electronic elements are
diodes
resistors,
capacitors,
inductors

## Slide 33: Ohm’s Law & Resistors
Assume that the wires are “perfect conductors”
The unknown circuit element limits the flow of current.
The resistive element has resistance R
Let us remind the Ohm’s Law
Georg Ohm
+
_
V
V
R = ——
I
V
I = ——
R

## Slide 34: Ohm’s Law
Voltage drop across a resistor is proportional to the current flowing through the resistor
If the resistor is a perfect conductor (or a short circuit)
R = 0Ω, then
v = iR = 0 V
no matter how much current is flowing through the resistor

## Slide 35: Resistors in Series

## Slide 36: Resistors in Parallel

## Slide 37: Resistors in Parallel

## Slide 38: Voltage Divider

## Slide 39: Equivalent Resistance – Complex Circuit

## Slide 40
Example: Calculate the current which is flowing through R4.

## Slide 41: CAPACITOR Energy Storage Device

## Slide 42: Maximum Charge on a Conductor
Earth
Battery
Conductor
-
-
-
-
-
-
-
-
-
-
-
-
-
-
e-
e-
A battery establishes a difference of potential that can pump electrons e- from a ground (earth) to a conductor
There is a limit to the amount of charge that a conductor can hold without leaking to the air. There is a certain capacity for holding charge.

## Slide 43: Capacitance
The capacitance C of a conductor is defined as the ratio of the charge Q on the conductor to the potential V produced.
Capacitance:
Earth
Battery
Conductor
-
-
-
-
-
-
-
-
-
-
-
-
-
-
e-
e-
Q, V

## Slide 44
The Capacitor
Capacitors are one of the fundamental passive components. In its most basic form, it is composed of two conducting plates separated by a dielectric material.
The ability to store charge is the definition of capacitance.
Dielectric
Conductors

## Slide 45
Initially uncharged
capacitor

## Slide 46
Charging

## Slide 47
Fully charged
After fully charged, a capacitor behaves as an open circuit and does not allow current flow.

## Slide 48
Source removed
A capacitor with stored charge can act as a temporary battery.

## Slide 49: INDUCTORs

## Slide 50: Electromagnetism
A wire carrying a current produces a magnetic field

## Slide 51
Inductance
Energy Storage Device
Stores energy in an magnetic field created by the electric current flowing through it.
The flow of current through an inductor creates a magnetic field
If the current flowing through the inductor drops, the magnetic field will also decrease and energy is released through the generation of a current.
B field

## Slide 52: Inductors
Conducting wire is wrapped around a solid core. If no core is used, then the inductor is said to have an ‘air core’.

## Slide 53: Voltage and Current Relation
Consider the circuit shown here
  inductor is initially un-energised
    current through it will be zero
  switch is closed at t = 0
  I is initially zero
    hence VR is initially 0
    hence VL is initially V
  as the inductor is energised:
    I increases
    VR increases
    hence VL decreases
    we have exponential behaviour

## Slide 54
Both the voltage and current have an exponential forms
L, inductance, has the unit of Henry (H)
1 H = 1 V.sn/A
C, capacitance, has the unit of Farad (F)
1 F = 1 A.sn/V

## Slide 55: Example 1
Determine I, the current flowing out of the voltage source.
  Use KCL
    1.9 mA + 0.5 mA + I are entering the node.
    3 mA is leaving the node.
    V1 is generating 3V.

## Slide 56: Example 2
If voltage drops are given instead of currents, you need to apply Ohm’s Law to determine the current flowing through each of the resistors before you can find the current flowing out of the voltage supply.

## Slide 57: Example 2 (con’t)
For power dissipating components such as resistors, current flows into the resistor at the terminal has the + sign on the voltage drop and leaves out the terminal that has the – sign.
I1 is leaving the node.
I2 is entering the node.
I3 is entering the node.
I is entering the node.

## Slide 58: Example 3
Find the voltage across R1. Note that the polarity of the voltage has been assigned in the circuit schematic.
  First, define a loop that include R1.

## Slide 59: Example 3 (con’t)
There are three possible loops in this circuit. Only two of them include R1. Either loop may be used to determine VR1.

## Slide 60: Example 3 (con’t)
If the outer loop is used, follow the loop clockwise.

## Slide 61: Example 3 (con’t)
    The 5V drop across V1 is a voltage rise.
    VR1 should be treated as a voltage rise.
    The loop enters on the positive side of the CURRENT source and exits out the negative side. This is a voltage drop as the voltage becomes less positive as you move through the component.
    Follow the loop in a clockwise direction.

## Slide 62: Example 3 (con’t)
Suppose you chose the green loop instead.
  Since R2 is in parallel with I1, the voltage drop across R2 is also 3V.

## Slide 63: Example 3 (con’t)
    The 5V drop across V1 is a voltage rise.
    VR1 should be treated as a voltage rise.
    The loop enters R2 on the positive side and exits out the negative side. This is a voltage drop as the voltage becomes less positive as you move through the component.
    Follow the loop in a clockwise direction.

## Slide 64: Example 4
Find the voltage across R2 and the current flowing through it. First, draw a loop that includes R2.

## Slide 65: Example 4 (con’t)
There are two loops that include R2.
  The one on the left can be used to solve for VR2 immediately.

## Slide 66: Example 4 (con’t)
  The 11.5V drop associated with V1 is a voltage rise.
  The 2.4V associated with R1 is a voltage drop.
  VR2 is treated as a voltage drop.
    Follow the loop in a clockwise direction.

## Slide 67: Example 4 (con’t)

## Slide 68: Example 4 (con’t)
If you use the right-hand loop, the voltage drop across R3 must be calculated using Ohm’s Law.

## Slide 69: Example 4 (con’t)
  Since R3 is a resistor, passive convention means that the positive sign of the voltage drop will be assigned to the end of R3 where current enters the resistor.
  As I1 is in series with R3, the direction of current through R3 is determined by the direction of current flowing out of the current source.
  Because I1 and R3 are in series, the magnitude of the current flowing out of I1 must be equal to the magnitude of the current flowing out of R3.
Use Ohm’s Law to find VR3.

## Slide 70: Example 4 (con’t)
Moving clockwise around the loop:
  VR3 is a voltage drop.
  The voltage associated with I1 is a voltage drop.
  VR2 is a voltage rise.
Again, the same answer is found.

## Slide 71: Example 4 (con’t)
  Once the voltage across R2 is known, Ohm’s Law is applied to determine the current.
  The direction of positive current flow, based upon passive sign convention is shown in red.
IR2

## Slide 72: Example 4 (con’t)
IR2