## Slide 1
EHB222E QUESTIONS
4th week

## Slide 2
A p-n diode is modeled with the exponential model. The diode currents are measured 1.36 mA and 7.20 mA when 0.7 V and 0.75 V applied, respectively. Determine the saturation current IS and the emission factor n (from nVT). Suppose that VT = 25 mV.

## Slide 3
Find the values of I and V for the circuits shown. Use ideal diode model (Vd=0) for diodes.
Ans. (a) 5 mA, 0V; (b) 0 mA, 5V; (c) 5 mA, 0V;
(d) 0.5 mA, 0V;

## Slide 4
Use a modified ideal model for the Zener diode in Figure 1. The model has 0,7 V forward bias and 2V Zener (VZ=2V) voltage. An input signal, shown in Figure 2, is applied. Sketch Vo, iD1 and iD2 in time domain. Justify your answer.
-2V
2V
0.7V
4.7V

## Slide 5
(b) VCC- (R1 +R2) ID2 – VD2=VEE
ID2=(VCC- VEE- VD2)/ (R1 +R2) =(10- (-10)-0.7)/15k=12.9mA (valid)
=-10V+5k 12.9mA+0.7=-2.86V (valid)
(b) = VD1-VEE= 10.7V (not valid)
In figure, assume modified diode model (VD=0.7V) for the diodes.
a) Calculate ID1 and VO for R1=5 kΩ, R2=10 kΩ.
b) Calculate ID1 and VO for R1=10 kΩ, R2=5 kΩ.
(b) = VCC-VEE= 20V (not valid)

## Slide 6
Figure Diode logic gates: (a) OR gate; (b) AND gate (in a positive-logic system).
In figure, assume ideal diode model (VD=0V) for the diodes. Calculate all possible output voltages. Input voltage (VA, VB, VC ) values are 5V or 0V.
Notes: sedr42021_0305a.jpg

## Slide 7
In figure, assume modified ideal diode model (VD=0.7V) for the diodes. Calculate output voltage.
(b) 10V - 15k ID2 – VD2= -10V , ID2=1.28mA (valid)
=-10V+10k 1.28mA=2.8V (valid)
(b) = 10V-(-VD1)= 10.7V (not valid)
(b) = 10-(-10) = 20V (not valid)
Notes: sedr42021_0306a.jpg

## Slide 8: All PN diodes shown below have a voltage drop of 0.6V when they are “ON”. Calculate output voltage with the given values (Va=4V, Vb=3V).