## Slide 1: BLG 231E – Recitation #5 Synchronous Sequential Circuits
Res. Ast. Tuğba PAMAY (2019 Fall)

## Slide 2: A Controller for a Simple Traffic Light
Assumptions:
2 linked pairs of traffic lights
Traffic flows:
  Right to left
  Bottom up
3 colors in a light: Red (R), Green (G), Yellow (Y)
«Yellow» light is for only before stop (Red light)

## Slide 3: A Controller for a Simple Traffic Light
One Light | Cross Light | Action
Green | Red | Traffic moving in one direction
Yellow | Red | Cars moving are preparing to stop.
Red | Red | Traffic in both roads stop for a second
Red | Green | Traffic moving in other direction
Assumed actions:

## Slide 4: Step #1: Name the States
State_ID | Light #1 | Light #2 | Alias
0 | Red | Red | RR
1 | Red | Green | RG
2 | Red | Yellow | RY
3 | Red | Red | RR
4 | Green | Red | GR
5 | Yellow | Red | YR

## Slide 5: Step #2: State Diagram
RR
RG
RY
RR
GR
YR
State_ID
0
1
2
3
4
5
Alias
RR
RG
RY
RR
GR
YR

## Slide 6: Step #3: Define State Table
RR
RG
RY
RR
GR
YR
Current State |  | Next State | 
State_ID | Alias | State_ID | Alias
0 | RR | 1 | RG
1 | RG | 2 | RY
2 | RY | 3 | RR
3 | RR | 4 | GR
4 | GR | 5 | YR
5 | YR | 0 | RR

## Slide 7: Step #4: How many FF do we need?
How many bits are enough to represent these states ?
  Formula:
  2 p-1 < N 2p
    N: number of states
    p: number of FFs
In our case :
N=6 => p= 3

## Slide 8: Step #4: How many FF do we need?
How many bits are enough to repreent these states ?
  Formula:
  2 p-1 < N 2p
    N: number of states
    p: number of FFs
In our case :
- N=6 => p= 3
- For each state => Q2 Q1 Q0

## Slide 9: Step #5: Assign 3-bit Binary Number to each state
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101

## Slide 10: Step #6: Derive the Output Equations
# of outputs:
2 traffic lights * 3 different colors: 6 outputs in total
R1, Y1, G1, R2, Y2, G2

## Slide 11: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.1: R1
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | ∅ | ∅
R1 =

## Slide 12: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.2: Y1
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | ∅ | ∅
Y1 =
Notes: The important is that we also cover the dont care bit beside the bit 1 for Y1 ?
Why ?
To reduce cost!

## Slide 13: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.3: G1
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 1 | 0 | ∅ | ∅
G1 =

## Slide 14: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.4: R2
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 1 | 0 | 1 | 0
1 | 1 | 1 | ∅ | ∅
R2 = +

## Slide 15: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.5: Y2
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 1
1 | 0 | 0 | ∅ | ∅
Y2 =

## Slide 16: Step #6: Derive the Output Equations
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Step #6.6: G2
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 0 | 0 | ∅ | ∅
G2 =

## Slide 17: Step #7: Derive State Transition Table
State_ID | Alias | Q2 Q1 Q0
0 | RR | 000
1 | RG | 001
2 | RY | 010
3 | RR | 011
4 | GR | 100
5 | YR | 101
Q2+ Q1+ Q0+
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 001 | 010 | 100 | 011
1 | 101 | 000 | ∅ | ∅

## Slide 18: Step #7: Derive State Transition Table
Q2+ Q1+ Q0+
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 001 | 010 | 100 | 011
1 | 101 | 000 | ∅ | ∅
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 00 | 01 | 00
1 | 11 | 10 | ∅ | ∅
Q2 Q2+

## Slide 19: Step #7: Derive State Transition Table
Q2+ Q1+ Q0+
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 001 | 010 | 100 | 011
1 | 101 | 000 | ∅ | ∅
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 01 | 10 | 11
1 | 00 | 00 | ∅ | ∅
Q1 Q1+

## Slide 20: Step #7: Derive State Transition Table
Q2+ Q1+ Q0+
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 001 | 010 | 100 | 011
1 | 101 | 000 | ∅ | ∅
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 01 | 10 | 10 | 01
1 | 01 | 10 | ∅ | ∅
Q0 Q0+

## Slide 21: Step #9: Derive Input Equations
# of inputs:
2 inputs * 3 JK FFs : 6 inputs in total
J0, K0, J1, K1, J2, K2

## Slide 22: Step #8: Select the Flip–Flops
JK Flip Flop
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0
Q = J +

## Slide 23: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | ∅ | ∅ | ∅ | ∅
J2 =
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 00 | 01 | 00
1 | 11 | 10 | ∅ | ∅
Q2 Q2+
J2
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0

## Slide 24: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | ∅ | ∅ | ∅ | ∅
1 | 0 | 1 | ∅ | ∅
K2 =
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 00 | 01 | 00
1 | 11 | 10 | ∅ | ∅
Q2 Q2+
K2
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0

## Slide 25: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 0 | 1 | ∅ | ∅
1 | 0 | 0 | ∅ | ∅
J1 =
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 01 | 10 | 11
1 | 00 | 00 | ∅ | ∅
Q1 Q1+
J1
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0

## Slide 26: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | ∅ | ∅ | 1 | 0
1 | ∅ | ∅ | ∅ | ∅
K1 =
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 00 | 01 | 10 | 11
1 | 00 | 00 | ∅ | ∅
Q1 Q1+
K1
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0

## Slide 27: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 1 | ∅ | ∅ | 1
1 | 1 | ∅ | ∅ | ∅
J0 = 1
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 01 | 10 | 10 | 01
1 | 01 | 10 | ∅ | ∅
Q0 Q0+
J0
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0

## Slide 28: Step #9: Derive the Input Equations
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | ∅ | 1 | 1 | ∅
1 | ∅ | 1 | ∅ | ∅
K0 = 1
Q1Q0 Q2 | 00 | 01 | 11 | 10
0 | 01 | 10 | 10 | 01
1 | 01 | 10 | ∅ | ∅
Q0 Q0+
K0
Q | Q+ | J | K
0 | 0 | 0 | ∅
0 | 1 | 1 | ∅
1 | 0 | ∅ | 1
1 | 1 | ∅ | 0