## Slide 1
MOSFET

## Slide 2
Field Effect Transistor (FET)
FET
JFET – Junction Field Effect Transistor:
  n-channel
  p-channel
MOSFET – Metal-Oxide-Semiconductor Field Effect Transistor:
  Enhancement-type:
    n-channel (NMOS)
    p-channel (PMOS)
  Depletion-type:
    n-channel
    p-channel

## Slide 3
MOSFET stands for metal-oxide semiconductor field-effect transistor.
Unlike BJT which is ‘current controlled’, the MOSFET is a voltage controlled device.
The MOSFET has “gate“, “Drain”, “Source” and “Body” terminals.
MOSFET
G-Gate
D-Drain
S-Source
B-Substrate or Body

## Slide 4
n-channel Enhancement-Type
MOSFET
Structure
p-type substrate
Two heavily-doped (n+) regions created in the substrate to form the drain and the source.
A thin (0.02 to 0.1 m) layer of silicon dioxide (SiO2) is grown on the surface of the substrate covering the area between the source and the drain.

## Slide 5
n-channel Enhancement-Type
MOSFET
SiO2 is an excellent insulator.
Metal is deposited on the top of the SiO2 layer to form the gate electrode.
Metal contacts are also made to the source region, drain region and the substrate.
Structure
Terminals are from these metal contacts which form the drain (D), source (S), gate (G) and substrate or body (B) terminals.

## Slide 6
MOSFET
With zero bias at the gate, the source and the drain are separated by the p-region – equivalent to two back-to-back diodes.
In this condition, the current is zero.
Operation
n-channel Enhancement-Type

## Slide 7
MOSFET
A gate voltage is required to create a conduction path.
The carriers in the conduction path are electrons – hence the term n-channel MOSFET (NMOS).
Operation
n-channel Enhancement-Type

## Slide 8
MOSFET
Current–voltage characteristics
In order to create to create a conduction path between , the gate-to-source voltage (vGS) must be applied to the gate of the transistor.
This voltage must be above a minimum value known as the threshold voltage (VTN) which is positive for NMOS.
vGS < VTN the channel is not formed
n-channel Enhancement-Type
Positive gate bias attracts electrons into channel.

## Slide 9
MOSFET
Current–voltage characteristics
When vGS exceeds VTN, the channel is formed and current will flow if a voltage is applied between the drain and the source (vDS).
This current is known as the drain current (iD)
n-channel Enhancement-Type

## Slide 10
MOSFET
Current–voltage characteristics
For small values of vDS, the channel depth is constant over the whole length from the source to the drain.
Constant channel depth
n-channel Enhancement-Type

## Slide 11
MOSFET
Current–voltage characteristics
The constant channel depth causes the MOSFET to operate as a linear resistance (indicated by the linear relationship between iD and vDS) whose value is controlled by vGS.
However, iD is zero for vGS < VTN for any value of vDS.
n-channel Enhancement-Type

## Slide 12: A voltage-controlled resistor @small VDS
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
- - - -
VGS1>Vt
G
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
+++
- - - - - -
VGS2>VGS1
p
n+
n+
metal
S
D
B
oxide
+
-
+++
+++
+++
- - - - - - - - -
VGS3>VGS2
+++
ID
VDS
0.1 v
increasing
VGS
Increasing VGS puts more charge in the channel, allowing more drain current to flow
cut-off
Positive gate bias attracts electrons into channel.
(Enhancement mode)
decreasing
resistance
G

## Slide 13
MOSFET
Current–voltage characteristics
As the drain voltage increases, the voltage drop along the channel increases from 0 to vDS.
The voltage between the gate and the points along the channel decreases from vGS at the source end to (vGS – vDS) at the channel end, resulting in a decrease in channel depth at the drain (Figure).
n-channel Enhancement-Type
This causes the conductivity to decrease.

## Slide 14
MOSFET
Current–voltage characteristics
As the drain voltage increases to the point where vGS – vDS = VTN, the channel depth will be zero.
The incremental conductivity is zero and the slope of the iD versus vDS curve is also zero. At the saturation point;
Or;
n-channel Enhancement-Type

## Slide 15
MOSFET
Current–voltage characteristics
For vDS > vDS(sat), iD is constant – saturation region
n-channel Enhancement-Type

## Slide 16
MOSFET
Current–voltage characteristics
As the vGS increases, the iD increases.
n-channel Enhancement-Type

## Slide 17
MOSFET
Current–voltage characteristics
The region where vDS < vDS(sat) is known as the triode region. For ideal MOSFET, the drain current iD in this region is given by the expression;
The region where vDS > vDS(sat) is known as the saturation region. The drain current iD in this region is given by the expression;
n-channel Enhancement-Type

## Slide 18
MOSFET
Current–voltage characteristics
The parameter Kn is called conduction parameter which for NMOS, is given by the expression;
n is the mobility of electrons in the inversion layer and Cox is the oxice capacitance per unit area given by the expression;
ox = oxide permittivity
tox = oxide thickness
n-channel Enhancement-Type

## Slide 19
MOSFET
Current–voltage characteristics
If we write;
the expression for Kn becomes;
The expression for the drain current in the saturation region becomes;
n-channel Enhancement-Type

## Slide 20
Field Effect Transistor (FET)
FET
JFET – Junction Field Effect Transistor:
  n-channel
  p-channel
MOSFET – Metal-Oxide-Semiconductor Field Effect Transistor:
  Enhancement-type:
    n-channel (NMOS)
    p-channel (PMOS)
  Depletion-type:
    n-channel
    p-channel

## Slide 21: Cross-Sectional View of n channel Enhancement Mode Transistor
Enhancement mode
Also known as Normally Off transistors.
▫ A voltage (at least equal to the threshold voltage) must be applied to the gate of the transistor to create a conduction path between the source and the drain of the transistor.
Cross-Sectional View of
p channel Enhancement Mode Transistor

## Slide 22: p channel Depletion Mode Transistor
n channel Depletion Mode Transistor
Depletion mode
Also known as Normally On transistors.
In order to prevent current from flowing between the source and drain, a voltage (at least equal to the threshold voltage) must be applied to the gate of the transistor to destroy the conduction path between the source and the drain.

## Slide 23
MOSFET
Circuit symbols and Conventions
Conventional symbol
Vertical broken line – the channel (broken line indicates the enhancement type
Vertical solid line – gate electrode
Separation – oxide layer
Arrowhead – polarity between the substrate and channel
n-channel Enhancement-Type
VGS ≥ 0V, VDS ≥ 0V
VTN is positive

## Slide 24
MOSFET
Circuit symbols and Conventions
n-channel Enhancement-Type
In many cases, the substrate and source terminals are connected together. The circuit symbol can be simplified.
The arrowhead is in the source terminal and direction indicates the direction of current.
VGS ≥ 0V, VDS ≥ 0V
VTN is positive

## Slide 25
MOSFET
Circuit symbols and Conventions
p-channel Enhancement-Type
VGS ≤ 0V, VDS ≤ 0V
VTP is negative

## Slide 26
MOSFET
Non-ideal Current–voltage characteristics
n-channel Enhancement-Type
The drain current iD is dependent on the drain-to-source voltage vDS due to channel length modulation.
Non-zero slope exists in the actual iD versus vDS characteristics beyond saturation point.

## Slide 27
MOSFET
Non-ideal Current–voltage characteristics
n-channel Enhancement-Type
Extrapolation on the characteristic curves produce a point of interception on the voltage axis at –VA.
 is the channel-length modulation parameter

## Slide 28
MOSFET
Non-ideal Current–voltage characteristics
n-channel Enhancement-Type
In the saturation region, the drain current may expressed as;

## Slide 29
MOSFET
Non-ideal Current–voltage characteristics
n-channel Enhancement-Type
The output resistance ro is the inverse of the slope of the characteristics curves;

## Slide 30
MOSFET
Non-ideal Current–voltage characteristics
n-channel Enhancement-Type
Differentiating the expression for iDS at the Q-point, gives us;
or

## Slide 31: Symbols for n channel Depletion Mode MOSFET
Symbols for p channel Depletion Mode MOSFET
in order to destroy the channel, gate voltage must be negative and less than the threshold voltage
An enhancement MOSFET and a depletion MOSFET are precisely identical in nearly every way (e.g., same modes, same equations, same terminal names).
Except: The threshold voltage for a depletion NMOS device is negative (i.e., Vt <0). While the threshold voltage for a depletion PMOS device is positive (i.e., Vt > 0).

## Slide 32
Load-Line Analysis
It is a graphical analysis similar to load-line analysis of pn diode.
Circuit Analysis:
Input
loop
Output loop
Load line
vGS
vDS
We look for the operating point

## Slide 33
Load-Line Analysis
Exercise:
Draw the Load line
RD= 1 kW

## Slide 34
Load-Line Analysis
Load line
Taking iD=0 or vDS=0 we draw the load line and the operating point Q for VGS=4V
Points A & B intersection of curve and the load-line for the maximum and the minimum gate voltage

## Slide 35
Input signal
Load-Line Analysis
(peak-to-peak amplitude is 2V)
12V peak-to-peak
Inverse operation
The positive peak of the input occurs at the same time as the min. value of vDS.
vDS(t)
vin(t)
2V peak-to-peak