## Slide 1
Operational Amplifiers

## Slide 2: Operational amplifiers (op-amps)
741 Amplifier is the most popular amplifier it has
Avo=100000 (voltage gain without load)

## Slide 3: Operational amplifiers (op-amps)
741 Amplifier BJT transistor level schematic

## Slide 4
Operational amplifiers (op-amps) are among the most widely used integrated circuits (ICs) in electronics.
A single package will often contain several op-amps

## Slide 5: Operational Amplifier Model
An operational amplifier circuit is designed so that
  Vout = A (V1-V2) (A is a very large gain)
  Input resistance (Rin) is very large
  Output resistance (Rout) is very low
V1
V2
Vout
Rin
+
-
Rout
A (V1- V2)

## Slide 6: Typical Op Amp Parameters
Parameter | Variable | Typical Ranges | Ideal Values
Open-Loop Voltage Gain | A | 105 to 108 | ∞
Input Resistance | Ri | 105 to 1013 Ω | ∞ Ω
Output Resistance | Ro | 10 to 100 Ω | 0 Ω
Supply Voltage | Vcc/V+ -Vcc/V- | 5 to 30 V -30V to 0V | N/A N/A

## Slide 7: An Ideal Operational Amplifier
Ri = ∞
Therefore, i1 = i2 = 0A
Ro = 0

## Slide 8: An Ideal Operational Amplifier

## Slide 9: An Ideal Operational Amplifier
A real op-amp must have a DC supply voltage which is often not shown on the schematics.

## Slide 10
Op-amps
Output voltage of an Op-amp can not be greater than DC supply voltage.
Maximum output voltage is usually slightly lower than the DC supply voltage and called as saturation voltage.

## Slide 11: Comparator
Applications: Low-voltage alarms, night light controller
V2
V1
Vout

## Slide 12: Pulse Width Modulator
Output changes when Vin ~= Vpot
Application: Motor controllers
  Vpot
  Vpot
  -Vsat
  +Vsat

## Slide 13: Negative feedback
Op-amp are almost always used with a negative feedback:
Part of the output signal is returned to the input.
Feedback reduces the gain of op-amp.
i1
i2
  Negative feedback forces the voltage at the inverting input terminal to be equal to the voltage at the noninverting input terminal.

## Slide 14: When A is very large:
Take A=106, R1=9R, R2=R
Gain now determined only by resistance ratio
Doesn't depend on A (or temperature, frequency, variations in fabrication).

## Slide 15: Why use Negative feedback?:
Makes properties predictable - independent of temperature, manufacturing differences or other properties of the opamp.
Circuit properties only depend upon the external feedback network and so can be easily controlled.

## Slide 16: More insight (Under negative feedback)
We also know
  i+ ≈ 0
  i- ≈ 0
Helpful for analysis (under negative feedback)
Two "Golden Rules«
1) No current flows into the op-amp
2) v+ ≈ v-

## Slide 17: Inverting Amplifier
v-= v+=0V
i1 = vin /R1
i2 = i1 and
vo = -i2 R2 = -vin R2 /R1
So
Av=vo /vin =-R2 /R1
i1
i2
Since negative feedback forces the voltage at the inverting input terminal (v-) to be equal to the voltage at the noninverting input terminal (v+), vx is equal to zero.

## Slide 18: Inverting Amplifier
Since vo = -i2 R2 = -vin R2 /R1
We see that the output voltage does not depend on the load resistance.
The output impedance of the inverting amplifier is zero.
The input impedance is: Zin=vin/i1=R1
Zin
Z0

## Slide 19: Summing Amplifier
The output voltage in summing amplifier is
vout=if*Rf since v-=v+=0

## Slide 20: Exercise
Find the currents and voltages in these two circuits:
a) i1=vin/R1=1V/1k Ω =1mA
i2=i1=1mA from KCL
vo=-i2*R2=-10V from KVL
io=vo/RL=-10mA from Ohms law
ix=io-i2=-10mA-1mA=-11mA
b) i1=vin/R1=5mA
i2=i1=5mA
i2*1kΩ= i3*1kΩ => i3=5mA
i4=i2+i3=10mA
vo=- i2*1k Ω - i4*1k Ω =-15 V
R1

## Slide 21: Exercise
i1
i2
i4
i3
i5
iL
V3
Find expression for the output voltage in the amplifier circuit:
i1=v1/R1=v1/10k Ω
i2=i1=v1/10mA
v3 =- i2*R2=- v1/10k Ω *20k Ω =-2v1
i5=i3+i4=v3/10k Ω +v2/10k Ω
vo =- i5*R5=-(v3/10k Ω +v2/10k Ω )*20k Ω =-2v3 -2v2 =4v1 -2v2

## Slide 22: Positive Feedback
When we flip the polarization of the op-amp as shown on the figure we will get a positive feedback that saturates the amplifier output.
This is not a good idea.

## Slide 23: Noninverting Amplifier
iL
i2
-i1
v1=vin
vin/R1 +(vin- vo)/R2=0
Thus the voltage gain of noninverting amplifier is:
Av= vo /vin = 1+ R2 /R1

## Slide 24: Voltage Follower
What's the application of this circuit?
Buffer
  voltage gain = 1
  input impedance=∞
  output impedance=0
Useful interface between different circuits:
Has minimum effect on previous and next circuit in signal chain

## Slide 25: Differential Amplifier (subtractor)

## Slide 26: Exercise
i1
i1
i2
Find voltage gain Av=vo/vin and input impedance
With the switch open
With the switch closed
Input impedance:
Zin=vin/iin =vin/0 =inf
a. With the switch open
i2=0 and i1*R=i2*R => i1=0
so vin=vo and Av=vo/vin =1

## Slide 27: Exercise
Find voltage gain Av=vo/vin and input impedance
With the switch open
With the switch closed
b. for closed switch: i2=vin/R
and i1*R=i2*R => i1=i2 => vin=i1*R+i1*R+vo
so vin=vin/R*R+vin/R*R+vo => -vin=vo
and Av=vo/vin =-1
i1
i1
i2

## Slide 28: Exercise
Find voltage gain Av=vo/vin and input impedance
With the switch open
With the switch closed
b. i2=vin/R
Input impedance: Zin=vin/iin =vin/(i1+i2)
and i1=i2 =>
Zin=vin/iin =vin/(2*vin/R)=R/2
i1
i1
i2

## Slide 29: Voltage to Current Converter
Find the output current io as a function of vin
vin =io*Rf
so
io=vin/Rf

## Slide 30: Exercise
Calculate the voltage gain vo/vin for R1=10 kΩ, R2 = 100 kΩ
Find the input resistance

## Slide 31: Exercise
From KCL1: vin/R1 +(vin-v2)/R2=0 => v2= vin (1+ R2 /R1)=11vin
From KCL2: (v2-vin)/ R2 +v2/R1+(v2-v0)/ R2 =0 =>
v0=(v2-vin) +v2R2/R1+v2 =>
v2
Calculate the voltage gain vo/vin for R1=10kΩ, R2 = 100 kΩ
Find the input resistance
v0 / vin =131

## Slide 32: Op-amp integrator
Integrator response to a constant voltage:
t
VIN
VOUT
VIN
VOUT
t
V
V
What's the integrator response to a square wave?

## Slide 33: Differentiating Op-Amp

## Slide 34: Op-Amp Imperfections in a Linear Mode
We consider the following op-amp imperfections:
Input and output impedances:
Ideal opamp
Real op-amp has

## Slide 35: Nonlinear Limitations
Nonlinear limitations:
Output voltage swing is limited and depend on power supply voltage for
Maximum output current is limited

## Slide 36: Nonlinear Limitations
When voltage or current limits are exceeded, clipping of the output signal occurs causing large nonlinear distortions

## Slide 37: Nonlinear Limitations
Another nonlinear limitation is limited rate of change of the output signal known as the slew-rate limit SR
Using slew rate (SR), we can find maximum frequency known as full-power bandwidth.
Assuming:
So the full-power bandwidth
maximum frequency

## Slide 38: DC offset values
There are three DC offset values related to op-amp design:
Bias currents IB+, IB- – related to differential inputs
Offset current – ideally zero value
Offset voltage – results in nonzero output for zero input
They can be represented as additional DC sources in the
op-amp model
İdeal OPAMP

## Slide 39: Resistor to balance the effect of bias currents