## Slide 1
EHB 222E
Introduction to Electronics
Week 3

## Slide 2: Semi-conductor

## Slide 3: Semi-conductor
Electron movement
Hole movement
 low friction, high μ
 high friction, low μ

## Slide 4: Semi-conductor
In an intrinsic silicon, at temperature 300 K:
Electron mobility = 1500 cm2/(V∙s) Hole mobility = 475 cm2/(V∙s)

## Slide 5: Semi-conductor
Why doping?

## Slide 6: Semi-conductor
Valance Band
Con duction Ban d
Silicon
1.1 eV

## Slide 7: Semi-conductor
Valance Band
Con duction Ban d
Germanium
0.66 eV

## Slide 8: Semi-conductor
Intrinsic Carrier
Due to random agitations from temperature
ni = po = eo = 1.5 x 1010 atoms/cm3
(Hence the name “semi”. Same number of carriers in its neutral form)
ni = p [cm ] x e [cm ]  This ratio is preserved
2 -3 -3

## Slide 9: Question 1
In an n-type material, the donor atom density is 10e17 atoms/cm3. What is free electron density?
Answer:
ND >> ni
Free electron density is 10e17 atoms/cm3 after doping

## Slide 10: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.

## Slide 11: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.
Region | Majority Carriers | Minority Carriers
n-type |  | 
p-type |  | 

## Slide 12: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.
Region | Majority Carriers | Minority Carriers
n-type | nn = ND = 1018 cm-3 | 
p-type |  | 

## Slide 13: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.
Region | Majority Carriers | Minority Carriers
n-type | nn = ND = 1018 cm-3 | pn = ni2/ND = 255 cm-3
p-type |  | 

## Slide 14: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.
Region | Majority Carriers | Minority Carriers
n-type | nn = ND = 1018 cm-3 | pn = ni2/ND = 255 cm-3
p-type | pp = NA = 1015 cm-3 | 

## Slide 15: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
a) Find majority and minority carrier concentrations in n- and p-type doped silicon.
Region | Majority Carriers | Minority Carriers
n-type | nn = ND = 1018 cm-3 | pn = ni2/ND = 255 cm-3
p-type | pp = NA = 1015 cm-3 | np = ni2/NA = 2.55 x 105 cm-3

## Slide 16: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
b) Find the barrier voltage.

## Slide 17: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
b) Find the barrier voltage.
i
n2


VB  VT ln


 N N
A D 

## Slide 18: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
b) Find the barrier voltage.
i
n2


 (1.5x1010 )2 
VB  VT ln
 25mV ln



  725mV
 1018 x1015

 N N
A D 

## Slide 19: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
c) Calculate the specific conductivities of n- and p-type doped silicon.

## Slide 20: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
c) Calculate the specific conductivities of n- and p-type doped silicon.
  q(nn p p )

## Slide 21
Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV
c) Calculate the specific conductivities of n- and p-type doped silicon.
 n qn ND 256 S / cm
 p q p N A 0.06 S / cm

## Slide 22: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?

## Slide 23: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?
𝑉 is found in the previous
𝐵
pages as 0.728 V
F = C/V

## Slide 24: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?

## Slide 25: Question 2
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?

## Slide 26: Question 1
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?

## Slide 27: Question 1
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
d) Determine the depletion zone width. How large is the depletion zone in n- and p-type regions around the junction?

## Slide 28: Question 1
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
e) What is the maximum of the electrical field in unbiased state?

## Slide 29: Question 1
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
e) What is the maximum of the electrical field in unbiased state?

## Slide 30: Question 1
You have a diode with the following doping properties: ND = 1018 cm-3 and NA = 1015 cm-3. ni = 1.5 x 1010 cm-3, q = 1.602 x 10-19 C, µn = 1600 cm2/Vs, µp = 400 cm2/Vs, VT = 25 mV,
𝜀𝑜 = 8.85 𝑥 10−12𝐹/𝑚, 𝜀𝑟 = 12
e) What is the maximum of the electrical field in unbiased state?